An Example of Total Functions

A Toaster

With

Important

Safety

Properties

by

Christopher Andrew Koeritz

November 1993

Abstract

Introduction

An Example ZENO Specification & the Resulting Ada Program

To demonstrate how a ZENO specification for a program might be used to assist verification, an example specification and program are presented here that will be informally shown to conform to aspects of a separate safety specification.

Due to the recursive definition for operations, total verification of an operation's consequences requires that the relationship between each interface and its implementation be proved from the top-level interface down to the underlying language or computer. This is essentially a proof of each level of the design. To demonstrate the proof process but not dwell on the details of each level, this demonstration is restricted to proving the relationship between one operation's interface and its implementation.

The specification for a Safety Toaster is the subject for property verification. While toasters do not commonly incorporate control programs or integrated circuits upon which to run them, it is interesting to consider how safety properties might be implemented for a particular toaster configuration. The simplicity of this example allows the safety properties to be stated in terms of the operations that interface with the toaster's sensor devices. In general, isolating safety properties is not this easy.

The underlying assumptions for this example are that the sensor devices are sufficiently reliable to provide the assurance desired and that the heat generated inside the toaster does not adversely affect the control program. One stringent requirement dominates the construction of the actual sensors; either the sensor reports accurate readings for the toaster, or it fails by producing a value that it could not possibly have measured within the toaster. The Safety Toaster control program relies upon the sensor devices to carry out its objectives.

A temperature sensor is used for the dual goals of determining the temperature at which the bread is being cooked and detecting if the bread inside the toaster is on fire. A somewhat redundant luminosity sensor is also available to the control program for reporting the light intensity inside the toaster. The light sensor can be used to detect if bread has been inserted in the toaster, and also whether the bread has caught on fire. Knowing if bread has actually been placed in the toaster allows the control program to avoid unnecessary heating.

An example of a sensor reading operation is shown in Figure for the Read_brightness operation. One consequence ( brightness_read ) reports the brightness measured by the luminosity sensor. The other three report important information about the state of affairs in the toaster either that the toaster is on fire, that there is no bread in the toaster, or that the luminosity sensor has failed.

The safety properties of the toaster are of the most concern here. It is desired that power to the toaster be turned off if the bread catches on fire. To make this goal possible, it is necessary that the toaster power relay be under software control, rather than under exclusively manual switch control as it is in most toasters. This ensures that if the toaster's push switch jams in the ‘down' position, the power to the toaster can still be turned off.

A top-level specification for the toaster control program is shown in Figure. This is a combination of the ZENO specification for the root operation with an Ada specification for the procedure implementing the ZENO specification.

The implementation of the toaster control program is shown in Figure, again as a mixture of ZENO and Ada. This will be automatically transformed by the ZENO translator into the full Ada implementation shown in Figure. The two major operations in the program are the Toasting and Safety_check operations. The Toasting operation carries out the functional aims of the toaster by applying heat to the toast until it has been in the toaster as long as the table of cooking times specifies. The Safety_check operation ensures that the toaster does not continue cooking the toast once the toast has caught on fire. Safety_check will be verified to conform to the following safety properties:

The toaster is turned off if there is no toast in it.

The toaster is turned off when the sensors indicate a fire inside the toaster.

The toaster is turned off if the sensors indicate that they have failed.

The first is not so much a safety property as an ‘‘idiot-proof'' property, because it ensures that the toaster is not heated when there is no reason to do so.

The specification for Safety_check is shown in Figure. The consequences of the sensor reading operations that indicate a violation of the safety properties have been promoted to the interface of Safety_check. This makes them accessible to the control program and it can react to them by shutting down the toaster power. The implementation of the Safety_check operation is shown in Figure with the additional ZENO notation necessary for connecting the consequences appropriately with management logic. The pure Ada Safety_check implementation is shown in Figure as it might be output by the translator.

The safety properties for this example can be stated as theorems to be verified in this way:

For all invocations of Read_Brightness that cause a No_Toast consequence, there exists an invocation of Power_Off within a short time span #delta#.

For all invocations of Read_Brightness or Read_Temperature that cause an On_Fire consequence, there exists an invocation of Power_off within a short time span #delta#.

For all invocations of Read_Brightness, Read_Temperature or Read_knob that cause a Sensor_error consequence, there exists an invocation of Power_off within a short time span #delta#.

The proof that these properties are guaranteed by the implementation of the toaster control program begins by examining the Safety_check implementation. Safety_check is the only operation that invokes any of the sensor reading operations it passes the sensed values to the Toast operation to simplify Toast 's implementation. Each of the consequences mentioned in the safety properties are contained in this operation, and each one is connected to the Power_off operation. Therefore, the safety properties are guaranteed given that the devices function properly. Again, the simplicity of this example enabled a painless proof of the properties. In a real program, the properties to be proved are significantly more complex, but they follow this general pattern for verification.