ZENO for Ada

<intro bit?>

In Ada, exceptions are bound to handlers dynamically, and thus the set of exceptions handled by a specific handler is not generally known until the program is executing. The postponement of this binding until run-time often means that anomalies are not discovered until the program is in the testing phase. An important goal of this research is to reduce the possibility of an undiscovered anomaly reaching the testing phase.

Asymmetry

<deverbosify>

<extract ada relevant for this section>

<extract relevant to

It is important to realize that the semantics of exception handling in existing languages are asymmetric. The exception handlers for an operation are textually separated from the statements for normal processing, and control-flow can occur between these two parts of the operation. However, the exception handling section’s semantics are not equivalent to the normal section’s semantics. The rules for a flow of control from the exception section to the normal section are different (and often significantly more complex) than the rules for a flow of control from the normal section to the exceptional section.

Exception handling has a very different intention than normal execution. Normal execution is intended to compute a result, while exception handling is intended to manage situations where a normal result cannot be computed []. This dichotomy can lead to program structures that are split by the dual requirements of normal processing and the handling of exceptions. Programmers often construct the normal regions of a program more carefully than the exception handling regions, possibly because they feel that their primary job is to create a functional program and that failure management (or more generally, exception handling) is not their responsibility. When a dependable program is to be created, this attitude will not suffice.

As an example of the effects that the asymmetry of exception handling can have on a programming language, consider the Ada programming language []. Figure  depicts a control flow graph for a hypothetical subprogram frame based on exception handling.

The arrows represent control-flows, while the nodes represent Ada statements or subprograms that are invoked as sub-operations. The left side of the graph represents the section of the operation that computes a standard functional result. The right side of the graph contains the exception handlers that manage situations where the standard result cannot be computed because an exception is raised. An exception can be handled by at most one handler, but handlers may handle an arbitrary number of different exceptions. If no handler is provided for a particular exception, then the exception exits the operation without being handled (for example, the bottom-most exception has no handler).

One asymmetry embodied in this figure is that control can flow to the exceptional side of the operation, but cannot flow back to the normal side. Another asymmetry is that only one type of standard result can be returned from the frame, while multiple exceptions can be raised by the operation. Cristian describes exceptions as separate exits from the operation []. If this interpretation is valid, then any Ada operation has n+1 total exits, where all standard results share one exit and there are n different exceptional exits. The numbers themselves seem to point to an asymmetry in the Ada exception model.

Anomalies

<use ada relevant anoms in ada appendix>

<suck out good definition and such property stuff into defins>

An anomaly is defined here as a problematical situation in a particular programming language’s semantics that can cause unexpected or undesirable behavior. Many programming languages have anomalies associated with them. For example, the FORTRAN programming language does not specify the meaning of a program after an exception is raised. However, there is the plausible interpretation that when a statement raises an exception, all of the statements appearing before that statement will already have been executed. Many FORTRAN compilers ignore this interpretation and reorder the statements for purposes of optimization, thereby making it impossible to determine the precise system state after an exception is raised.

In a large programming language, anomalies can arise from the complexity of the syntax and semantics, from the difficulty of seamlessly integrating the language features together, and from the difficulty of correctly using the semantics. In the case of the Ada programming language, the exception handling mechanism is integrated with the mechanisms for generic units, tasking, and subprograms. In Ada, the integration is not perfect. Ada is complex and has many anomalies associated with it, yet it is used for building applications that must be dependable or even safety critical []. For this reason, the programming language Ada is chosen as a motivating example for this research.

A catalog of the known Ada exception handling anomalies is recorded in []. To date, twenty anomalies have been discovered. These Ada anomalies can be considered to arise from three primary causes: 1) the semantic model for Ada exception handling, 2) the interactions between that model and other parts of the language, and 3) programming that is done without full understanding of 1) or 2).

Ada’s exception handling semantics do not prohibit the inclusion of anomalies in programs. These anomalies are not only hard to locate and eliminate from the program, they are also dangerous because they can cause the program to violate critical aspects of its specification (such as its shut-down policy, the consistent state of its variables, its timely processing of data, and so forth). The following sections provide a few examples of the Ada exception handling anomalies.

Uncontrolled Propagation Anomaly

An example of an anomaly arising from the first cause (the semantic model) is the uncontrolled propagation anomaly. Exception propagation is the process of signalling the invoker of an operation that the operation could not compute a normal result. This means that an invoked operation can raise an exception in the invoker to signal an exceptional exit of the operation. The Ada programming language has a multi-level termination model, meaning that exception frames (or program blocks) can be terminated but not resumed when an exception is raised and that multiple invocation frames can be terminated by an exception before it is handled. The anomaly of uncontrolled propagation results from this interpretation of propagation and the fact that, although exceptions can be declared as existing, they cannot be declared as propagable. In other words, an Ada operation’s exception handling behavior is not fully specified, because exceptions might be propagated to the invoker without a prior specification of that possibility.

Because there are no semantics for declaring propagable exceptions and because Ada does not automatically generate the set of propagable exceptions, unexpected exceptions can propagate to an invoking operation. Thus it is possible for an exception to propagate beyond the point where it is most effectively handled. When an exception does this, it is said to propagate in an uncontrolled manner. An uncontrolled propagation can actually terminate the program if the exception propagates to the outermost subprogram.

An exception handler for others handles any exception, as long as the exception has no explicit handler listed for its name. Thus an exception cannot propagate out of an operation before the others handler is invoked. This is an effective stopgap measure for controlling propagation, but the others handler can usually only perform the most general handling of the exception. If more specific information were available in the program for handling that exception, the information would have been encoded as an explicit handler for the exception. Also, because the others handler can invoke arbitrary sequences of Ada operations that might raise exceptions, the others handler itself might propagate an arbitrary number of exceptions. This is a reason why programs should be constructed from dependable code fragments and why ad hoc handlers for others are to be avoided; whereas the code fragments can be verified intensively before being used in numerous operations, the ad hoc handlers must be verified independently each time a new operation is created.

Uncontrolled propagation is a serious deficiency because it is not easy to determine the set of exceptions that can actually be propagated. If a programmer is to handle the full set of exceptions that can propagate from an invoked Ada operation, the programmer must examine the implementation of the invoked operation and the implementations of all operations invoked by that invoked operation, continuing down the invocation graph until only basic Ada operations remain to be examined. This situation is taxing for the programmer and does not assist in the program design process.

Deadlock due to Propagation Delay Anomaly

An anomaly arising from the second cause of anomalies (adverse interaction of the exception mechanism with another mechanism) is the deadlock due to propagation delay anomaly. This anomaly arises from an interaction between the Ada exception handling mechanism and the Ada tasking mechanism. Section 11.4.1.9 of the Language Reference Manual states that exception propagation is delayed when dependent tasks have not completed []. This rule causes a program deadlock when:

a task is instantiated in a frame,

an exception raise circumvents rendezvous with the task, and

propagation is delayed awaiting the task’s completion.

If a program encounters a tasking deadlock, then no further results are computed by the locked sections of the program. If the root operation of the program is involved in the deadlock, then the program will never complete of its own accord.

Anonymous Exception Anomaly

Another anomaly arising from the second cause of anomalies is the anonymous exception. This anomaly arises from the interaction between the exception handling mechanism and the Ada scope rules. Exceptions have both static and dynamic attributes in Ada. Exceptions are handled dynamically, but are declared statically. Because exceptions have static scope, they are visible only within the scope of their declaration. If an exception is dynamically propagated to a scope where its declaration is not visible, then that exception becomes anonymous. An anonymous exception effectively loses the mapping between its name and its dynamically propagating occurrence. An anonymous exception cannot be handled using its original name, and thus it can only be handled by an others handler. This means that any handlers intended for the exception are inaccessible once it becomes anonymous, even if the exception propagates back to a scope where it can normally be named under the static scoping rules.

Deadlock due to Propagation Delay

This figure shows a program that will encounter a deadlock anomaly:

Ada Exception Handling Semantics

Although the Ada Language Reference Manual [] is fairly precise, its form and content do not make its implications apparent. Many notes about exception handling are strewn throughout the LRM, rather than being contained in the exception handling section. By grouping all language-defined information regarding exception handling in one document [], reading the LRM many times can be avoided. For clarity, a summary of the Ada exception handling semantics is presented here.

The Ada semantics define that an exception must be declared within a scope, much as variables are. The scope of an exception might be:

a procedure or function, both of which are called sub-programs in Ada,

a block, the smallest ‘part' out of which sub-programs are constructed,

a task, the construct for concurrency in Ada, or

a package, an object-based mechanism for implementing abstractions composed of tasks and sub-programs.

Exceptions are raised to signal that an exceptional condition has been detected. Exceptions are raised in a frame, which is the representation during execution of one of the four scopes described above. When a frame is invoked, it either completes normally or it raises an exception.

A group of exception handlers can be attached to the bottom of any frame. A handler is activated when its exception is raised in the frame. If the handler itself does not raise any exception, then its own exception is said to be masked. A masked exception raise is treated by the invoker exactly as if the invoked frame completed normally. A handler for the special name others can be provided to handle any exceptions that have no other exception handlers in the frame.

An exception can propagate to the invoker of a frame. Propagation means that the exception is raised again inside the invoker (at the point where it invokes the frame propagating the exception). Propagation occurs if one of the following is true for the frame in which an exception is raised:

the exception has no handler in the frame,

the handler raises the exception again,

or the handler raises another exception.

Note that in the third case, the propagated exception is different from the one raised initially.

ZENO: A Specification Notation

Supplementing a traditional programming language with a small specification language based upon the consequence model can enhance program dependability by a very large degree. Consequences are the basis of the language, not only to avoid the pitfalls of current models based on the exception, but also because the consequence is general, allows the kind of control that designers of dependable applications need, and because it provides for the essential needs of exception handling without enforcing an inappropriate model. The initial problem of ‘‘what is wrong with exception handling in Ada?'' has been generalized to ‘‘how can programs be designed to ensure that certain properties of their specifications hold?'' The answer to both questions is: there needs to be a specification of exactly what operations have multiple outcomes, and exactly how these outcomes are related to the operands. The ZENO language addresses these issues and provides a workable solution to the problem of program verification for dependability.

Stuff about ZENO that needs to be cleaned way up:

<remember: operations are now the unified construct. different flavors can be used differently. the ada virtual machine is defined in terms of the ada sequential op and the ada task, where the zone is provided as a cleaner(?) interface to the task. there’s both the issue of modelling the language in operations and the issue of providing nice features to the ada programmer. tasks will be modelled, zones will be provided>

ZENO Description

The specification notation as it is currently conceived has three major constructs: the element, the operation, and the zone. The element contains static data, the operation manipulates elements, and the zone structures concurrent operations. Each construct is defined hierarchically according to a precise format. New members of elements, operations and zones can be composed recursively from pre-existing members.

Elements

Elements contain data in a variety of formats, many of which will be provided by the underlying language or computer of implementation. Elements can be composed from other elements, and can be passed through a filtering operation to extract one part of the element. Unlike the objects of object-oriented programming, elements have no methods associated with them; without operations they are utterly static, although they might have certain static characteristics specified in their definition.

An element's characteristics can include domain specific knowledge or assertions about the element type. For example, an integer element type might define MAXINT to be the largest representable integer. The MAXINT name can then be used to define operations on integers that do not require their specifications to be modified when the underlying machine is changed; only the MAXINT value associated with the element needs to be modified to allow the operation's specification to be used on that machine.

Another example element is a communications port. The port can represent different pieces of port status information as a corresponding bit pattern held in a segment of the port's logical pins. The element definition for the port would describe these patterns and associate a name with them to allow operations to be independent of the actual bit patterns. This allows information regarding the port element to be described formally, which in turn can simplify the operations using the element.

Operations

Operations take elements as their operands. Application of an operation to its operands yields one consequence as its conclusion. Each consequence is composed of an outcome and result where the result is the data that flows on a particular outcome path. The outcome of an operation can be connected to another operation, called a successor, when the result matches one or more of the operands of the successor. Operations are thus strongly typed, but flexible in that elements can be composed and decomposed at will.

Zones

The zone construct is used to specify concurrent programs within the consequence model. Each zone has a boundary around it to ensure that no zone can affect another zone's computation other than through the message passing mechanism. The boundary prohibits a variable from being used by more than one zone at a time, and this removes the need for synchronizing access to the variable. Should a common data source be needed, a zone can be used to grant or deny access to the data source.

A zone accepts a set of operand messages and can generate a set of consequence messages. Each operand message is a request for a particular service from the zone and it is connected to a single operation that processes it. The service requests are queued until the zone is free to work on them although zones are concurrent with each other, activity within a particular zone is sequential (excluding its sub-zones). Since operations are arbitrarily large, a single operation for each service request is sufficient because the operation can decode the message, compute a result and send a reply message. Consequences of the operation processing a message can: 1) become the consequence messages of the zone, 2) be deferred to a sub-zone for processing, or 3) not generate any consequence message at all.

An example zone is shown in Figure. This is a simple zone that controls access to a system's real time clock. Two services are provided; one for setting the clock and the other for reading the time. Communication delay might of course render the time reading slightly out of date, but this clock is not intended for fine granularity computations.

Zones ease program construction when using tasking by following the same model as total operations, and they provide some analogous properties to the sequential operation in the multi-processing environment. The properties of a zone result from the properties of the operations comprising it, and there is a separation between aspects of the zone communication and aspects of the zone computation that is felt necessary to effectively reason about concurrent operations.

# Footnotes

The assistance of the MITRE Corporation is gratefully acknowledged; in particular, Chuck
Howell, Diane Mularz and Gary Bundey helped define the various problems in Ada.